## Slide 1: Raspberry Pi Setup

## Slide 2: Goals
Install Raspbian
Connect to Pi

## Slide 3: Installing Raspbian
https://www.raspberrypi.org/downloads/raspbian/
1. Download Raspbain

## Slide 4: Install Etcher
https://etcher.io/
2. Install Etcher

## Slide 5: Flash disk with Raspbian image
3. Open etcher and select the Raspbian.zip file

## Slide 6: Flash disk with Raspbian image
4. Plug in sd card and select it

## Slide 7: Flash disk with Raspbian image
5. Begin flashing image

## Slide 8: Flash disk with Rasbian image
6. Wait to finish

## Slide 9: Edit System Files
Unplug and replug in sd card on your computer
Enter boot partition
Create empty ‘ssh’ file
Create wpa_supplicant.conf

## Slide 10: Edit System Files
1. Enter boot partition

## Slide 11: Edit System Files
2. This is best done in terminal on Mac and git bash on Windows
Right click in directory to open this menu on Windows
On Mac open terminal and go to /Volumes/boot

## Slide 12: Edit System Files
3. Create ssh file by typing this

## Slide 13: Edit System Files
4. Create wpa_supplicant.conf file

## Slide 14: Edit System Files
5. Copy the first 3 lines in verbatim
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=US

## Slide 15: Edit System Files
6. Enter your network specifics
Wifi network name
Wifi network password
Wifi network security type
Example should work in most cases

## Slide 16: Edit System Files
7. It is possible to have multiple networks
Wifi network name
Wifi network password
Wifi network security type
Example should work in most cases
Wifi network priority
When multiple networks are available, the network with the highest priority will be selected. In this case PiNet because 2 > 1

## Slide 17: Edit System Files
8. Save file and eject the sd card

## Slide 18: RaspberryPi internal ip address
This is probably the hardest part
We are going to try to find the ip address of our pi
There are 3 ways we can do this
  2 Do not require using an external monitor
  1 requires an external monitor

## Slide 19: RaspberryPi internal ip address
Method 1: Find ip address through your router interface
  This is the method we did today
We assigned/reserved ip addresses so they do not change on us the next time we use them. Usually every 24 hrs
User’s Pi permanent internal ip address
User’s Pi temporary internal ip address

## Slide 20: RaspberryPi internal ip address
Method 2: Find ip address through 3rd party app
In this case I used Fing. Fing is a popular application available for both android and iOS. All you have to do is be on the same network as your Pi and it will show up
My Pi’s ip address

## Slide 21: RaspberryPi internal ip address
Method 3: Plug your pi into a monitor and look it up manually
Enter this command
Your internal ip address

## Slide 22: ssh into your pi
1. Run this command to ssh into your pi. Replace the ip address with your ip address from the previous section

## Slide 23: ssh into your pi
2. Type yes to accept

## Slide 24: ssh into your pi
3. Enter your password. The default password is ‘raspberry’. Although no text appears, your input is being recorded

## Slide 25: ssh into your pi
4. Assuming everything was done correctly, you are now connected to your pi

## Slide 26: Enable VNC
1. While connected to your pi enter this command

## Slide 27: Enable VNC
2. Using the arrow keys, type down to option 5 Interfacing Options and hit enter

## Slide 28: Enable VNC
3. Using the arrow keys, type down to option 3 VNC and hit enter

## Slide 29: Enable VNC
3. Using the arrow keys, select yes and hit enter

## Slide 30: Enable VNC
4. VNC is now enabled

## Slide 31: Enable VNC
5. Using the arrow keys, type right to highlight finish and hit enter to exit

## Slide 32: Download a vnc viewer you don’t have one
https://www.realvnc.com/en/connect/download/viewer/

## Slide 33: Using VNC Viewer
Type your ip address into the search bar and hit enter

## Slide 34: Using VNC Viewer
Select continue

## Slide 35: Using VNC Viewer
Your default username will be ‘pi’ and your default password will be ‘raspberry’
Hit Ok to connect

## Slide 36: Using VNC Viewer
You will most likely be shown a low resolution display like this

## Slide 37: Using VNC Viewer
Click the raspberry in the top left corner, then navigate and select this option

## Slide 38: Using VNC Viewer
This is where you will go to change your password. Also you can change your hostname to make your pi a little easier to identify
Select this and scroll down to the last option

## Slide 39: Using VNC Viewer
This is where you will go to change your password. Also you can change your hostname to make your pi a little easier to identify
Select this then hit okay

## Slide 40: Using VNC Viewer
Select okay to save your changes. You may need to drag the Raspberry Pi Configuration window to the top of the desktop in order to see and select the okay option
Select this then hit okay. It will ask you to reboot select yes

## Slide 41: Using VNC Viewer
You are now greeted with a pretty display and can now begin playing around with your pi from your own computer